# collect_temp.py – Baseline Requirements
## 1. Purpose
collect_temp.py is a Python-based temperature data collector designed to run on a Raspberry Pi Zero 2. It:
- Periodically acquires temperature measurements from DS18B20 1-Wire sensors on two GPIO-based buses.
- Buffers data and outputs it to one or more destinations:
  - Console debug
  - SQLite database
  - MQTT broker
- Uses aligned, deterministic timing for acquisition and flush cycles.
This document represents the authoritative requirements baseline derived directly from the current working implementation.

## 2. Hardware & OS Assumptions
- Platform: Raspberry Pi Zero 2
- OS: Linux with 1-Wire support enabled
- 1-Wire overlay configuration:
  - Two dtoverlay=w1-gpio instances
  - GPIO pins are fixed and static
- Expected sysfs paths:
  - /sys/bus/w1/devices/w1_bus_master1
  - /sys/bus/w1/devices/w1_bus_master2
Note: Hardware configuration is assumed static during runtime.

## 3. Sensors
- Type: DS18B20
- Identified by unique 1-Wire serial numbers (28-xxxxxxxxxxxx)
- Sensors may appear on either bus
- Discovery occurs once at startup
- Invalid readings are recorded as None
- Sensor names:
  - Loaded from sensors.cfg if known
  - Otherwise, assigned as unknownN
- Sensor names are used as keys in records, DB columns, and MQTT payloads

## 4. Discovery Behavior
- Startup scans both 1-Wire bus directories
- Any entry beginning with 28- is treated as a valid sensor
- Global sensor map constructed as:
serial → {"name": <sensor_name>, "bus": <bus_path>}
- When DEBUG = True, discovery prints:
  - Bus name and path
  - Each sensor found per bus with assigned name
  - Final count of total sensors discovered
- Discovery is silent when DEBUG = False
- sensors.cfg is updated with newly discovered sensor names

## 5. Timing Model
### 5.1 Read Timing
- READ_RATE defines acquisition interval (seconds)
- Acquisition is epoch-aligned using modulo arithmetic
- At startup, program waits until next alignment boundary
- Acquisition cycle:
  - Record trigger epoch (Unix timestamp)
  - Issue Convert-T trigger to all buses
  - Wait fixed conversion delay (CONVERSION_DELAY = 0.9 s)
  - Read all sensor values
### 5.2 Conversion
- All buses with sensors are triggered sequentially
- Single fixed delay after trigger used before reading sensors
### 5.3 Write Timing
- WRITE_RATE defines flush interval for buffered records
- Flush occurs in blocks of WRITE_RATE / READ_RATE records
- Writes are attempted once per flush

## 6. Temperature Processing
- Raw temperature read from /sys/bus/w1/devices/<serial>/w1_slave
- CRC must pass (YES in first line)
- Default power-on value (85.0°C) is rejected
- Valid readings:
  - Converted to Fahrenheit
  - Rounded to nearest 0.1°F
  - Stored as int16 (°F × 10)
- Errors or invalid readings yield None

## 7. Data Record Structure
Each record consists of:
- epoch (INTEGER):
  - Unix timestamp of conversion trigger
  - Monotonic and unique
- temps (dictionary):
  - Key: sensor name
  - Value: int16 temperature or None

## 8. Output Modes
Output is controlled by independent boolean flags; multiple can be enabled simultaneously.
### 8.1 DEBUG Mode (DEBUG = True)
- Prints sensor discovery details
- Prints each acquisition line:
MMDDYYYY HH:MM:SS sensor_name: value
- Logs buffer flush events
- Logs internal errors (conversion, DB, MQTT)
- DEBUG output is print-only, no side effects

## 9. SQLite Output (DB_WRITE)
### 9.1 Database
- SQLite database located at DB_PATH
- Single table named TABLE_NAME
### 9.2 Schema
- Table created if not existing
- Columns:
  - epoch INTEGER PRIMARY KEY
  - One column per sensor (sensor name, INTEGER)
- New sensors discovered at startup:
  - Missing columns added automatically
  - Silent schema evolution
### 9.3 Inserts
- Every insert includes all known sensor columns
- Missing/failed readings stored as NULL
- Epoch uniqueness enforced by PRIMARY KEY

## 10. MQTT Output (MQTT_WRITE)
### 10.1 Broker Model
- Local-LAN MQTT broker required (e.g., Mosquitto)
- Collector acts as publisher only
### 10.2 Connection
- Broker: MQTT_BROKER
- Port: MQTT_PORT
- Optional username/password
- Keepalive enabled
- Uses paho-mqtt Callback API v2
### 10.3 Topic
Single publish topic: MQTT_TOPIC
### 10.4 Payload Format
{
  "device": "rpi-zero-2",
  "table": "Temperature",
  "records": [
    {
      "epoch": 1706001234,
      "temps": {
        "sensor_name_1": 697,
        "sensor_name_2": null
      }
    }
  ]
}
- Mirrors SQLite semantics
- null for missing values
- Entire buffer published per flush
### 10.5 Reliability
- Best-effort publish
- Failures logged in DEBUG mode
- No retained messages

## 11. Buffering & Error Handling
- Single shared buffer fans out to DB and MQTT
- Flush occurs when buffer reaches records_per_block
- On flush:
  - Errors logged in DEBUG mode
  - No automatic retry; buffer is dropped on failure
- Normal mode is silent

## 12. Shutdown Behavior
- SIGINT / SIGTERM initiate shutdown
- Acquisition loop exits cleanly
- One final best-effort flush attempted
- MQTT loop stopped and client disconnected

## 13. Non-Goals / Explicit Exclusions
- No dynamic sensor hot-plug during runtime
- No cloud connectivity
- No subscription-based MQTT logic
- No retry persistence across restarts
- No Perc-o-Matic or unrelated systems

## 14. Configuration Defaults (Baseline)
- READ_RATE: 15 seconds
- WRITE_RATE: 60 seconds
- CONVERSION_DELAY: 0.9 seconds
- DEBUG: enabled
- DB_WRITE: enabled
- MQTT_WRITE: enabled