# collect_temp.py — Authoritative Requirements (Current Implementation)
## 1. Purpose
collect_temp.py is a deterministic temperature data acquisition service designed to run continuously on a Raspberry Pi Zero 2.
It:
- Acquires temperature data from DS18B20 sensors on two 1-Wire GPIO buses
- Uses strictly epoch-aligned timing for repeatable sampling
- Buffers records in memory
- Periodically flushes data to:
  - SQLite database
  - MQTT broker (optional, disabled by default)
  - Console debug output
- Is designed for predictable, repeatable logging, not resilience or networking complexity
This document is derived directly from the current working source code.

## 2. Hardware & OS Assumptions
- Platform: Raspberry Pi Zero 2
- OS: Linux with 1-Wire support enabled
- Two static overlays configured:
/sys/bus/w1/devices/w1_bus_master1
/sys/bus/w1/devices/w1_bus_master2
Hardware and bus configuration are assumed static for the duration of program execution.

## 3. Sensors
- Type: DS18B20
- Identified by 1-Wire serial: 28-xxxxxxxxxxxx
- Sensors may exist on either bus
- Sensors are discovered once at startup
- No runtime hot-plug detection
- Invalid readings recorded as None
### 3.1 Sensor Identity Model (Critical)
Sensors are not keyed by name internally.
Each sensor is assigned a column serial:
column_serial = raw_serial with "-" replaced by "_"
28-00000abc1234 → 28_00000abc1234
This column serial is used for:
- Record storage
- SQLite column names
- Internal ordering
### 3.2 Human-Readable Names
A configuration file temp.cfg stores:
<raw_serial> <name>
Unknown sensors are assigned:
unknown1, unknown2, ...
This file is automatically updated during discovery.
Human names are used only for:
- Debug output
- MQTT payloads

## 4. Discovery Behavior
At startup:
1. Both bus directories are scanned
2. Any entry beginning with 28- is treated as a sensor
3. Global structures created:
sensors[column_serial] = {
    name,
    bus,
    raw_serial
}

sensor_order = [column_serial, ...]
temp.cfg is rewritten if new sensors are found
### 4.1 DEBUG Discovery Output
When DEBUG = True:
- Bus path printed
- Each sensor printed with assigned name
- Final summary printed
When DEBUG = False, discovery is silent.

## 5. Timing Model
Parameter	Value	Meaning
READ_RATE	30 s	Acquisition interval
WRITE_RATE	300 s	Flush interval
CONVERSION_DELAY	0.9 s	Sensor conversion time

### 5.1 Epoch Alignment
Sampling is aligned to wall-clock epoch boundaries:
next = now + (rate - (now % rate))
At startup, the program waits until the next alignment boundary.

## 6. Acquisition Cycle
At each aligned epoch:
1. Record trigger epoch timestamp
2. Trigger conversion on each bus via w1_master_slaves
3. Sleep CONVERSION_DELAY
4. Read every sensor from /sys/bus/w1/devices/<raw>/w1_slave

## 7. Temperature Processing
A reading is valid only if:
- CRC line contains YES
- Temperature is not 85.0°C
Valid readings:
1. Converted to Fahrenheit
2. Rounded to nearest 0.1°F
3. Stored as integer: °F × 10
Failures return None.

## 8. Record Structure (Internal)
Each buffered record:
{
  "epoch": <int>,
  "temps": {
      column_serial: value_or_None
  }
}

## 9. DEBUG Mode
When enabled:
- Discovery information printed
- Each acquisition prints:
MMDDYYYY HH:MM:SS name: value name: value ...
- Flush events printed
- Shutdown flush printed
No side effects.

## 10. SQLite Output (DB_WRITE)
### 10.1 Database
/var/lib/logger/database/temperature.db
Table: "Temperature"
### 10.2 Schema
On startup:
epoch INTEGER PRIMARY KEY
s<column_serial> INTEGER
Example:
s28_00000abc1234
### 10.3 Schema Evolution
- New sensors automatically add new columns
- No columns are removed
- Missing readings stored as NULL
### 10.4 Inserts
Every insert includes all sensor columns.
Epoch uniqueness enforced by PRIMARY KEY.

## 11. MQTT Output (MQTT_WRITE)
Disabled by default.
### 11.1 Role
MQTT is a read-only consumer of the buffer, identical to SQLite.
### 11.2 Connection
- Broker: MQTT_BROKER
- Topic: MQTT_TOPIC
- Uses paho-mqtt Callback API v2
- Automatic reconnect on unexpected disconnect
### 11.3 Payload Translation (Important)
Before publishing, records are translated:
column_serial → sensor name
MQTT payload uses human-readable names.
### 11.4 Payload Format
{
  "device": "rpi-zero-2",
  "table": "Temperature",
  "records": [
    {
      "epoch": 1706001234,
      "temps": {
        "LivingRoom": 697,
        "Outdoor": null
      }
    }
  ]
}
Entire flush block is published as one payload.

## 12. Buffering & Flush Behavior
- Records appended to shared buffer
- Flush occurs when:
len(buffer) >= WRITE_RATE / READ_RATE
- Same block sent to DB and MQTT
- No retry logic
- Errors only visible in DEBUG output

## 13. Shutdown Behavior
On SIGINT / SIGTERM:
1. Loop exits
2. Remaining buffer flushed once
3. MQTT cleanly disconnected (if enabled)

## 14. Configuration Defaults
Setting	Default
DEBUG	True
DB_WRITE	True
MQTT_WRITE	False

## 15. Explicit Non-Goals
The program intentionally does not implement:
- Runtime sensor hot-plug
- Retry or persistence on failures
- Dynamic bus configuration
- Cloud connectivity
- Subscription-based MQTT logic

## 16. Architectural Principles
1. Sensors are keyed by column serial, not name
2. SQLite columns are "s" + column_serial
3. MQTT uses names only as a presentation layer
4. Timing is strictly epoch-aligned
5. Discovery occurs once at startup
6. Design favors deterministic logging over resiliency